## Slide 1
INTRODUCTION TO EMBEDDED PROGRAMMING
Notes: Hey guys welcome to week 21
We’re going to go through an intro into microcontrollers with the goal of trying to link our already familiar Arduino Nanos from the Bintroduction to electronics
To STM32 microcontrollers
We’ll go through
reading pinout schematics
Understanding the workings of
  Digital pins, analog pins and basic communication protocols

## Slide 2: MICROCONTROLLERS
M
Notes: A microcontroller is a small computer on a single integrated circuit. A microcontroller contains one or more CPUs along with memory and programmable input/output peripherals.
This is reminiscent to a city where different parts of the microcontroller are responsible for different operations. Also, different cities vary in size, complexity and functionality just as microcontrollers do. Furthermore, each city may use a multitude of languages to communicate information across it's information dense network. The only thing a city doesn't have is a datasheet rich of highly detailed technical information of how these small subsystems interconnect with the outside world.

## Slide 3
WHAT IS AN DIGITAL PIN?
Digital High
Digital Low
1
0
0.5VCC
0.3VCC
Notes: Digital Pin
Can be an input or an output
As an INPUT:
  Takes a reading from the pin -> depending on the voltage value it either returns a 1 or a 0 based on where the voltage fits within the figure shown above
  Vcc is the microcontrollers supply voltage which is 5V for the Arduino NANO
  The input is sensitive to current and must be protected by a resistor where appropriate.
As an OUTPUT:
  In the microcontrollers code the pin can be set to high or low
    Where High is Vcc
    And Low is GND
  As an output it can only supply a low power signal and shouldn’t be used to power devices directly
Where these are commonly used
  Input:
    Buttons
    Switches
    State machine variables -> any time we want the microcontroller to do something after we tell it to and a multitude of different ways.
  Output:
    Tell another component to activate
      Sensors
      Another microcontroller
    Signal generation
      PWM, Clock signals etc.

## Slide 4
WHAT IS AN ANALOG PIN?
5V
0V
ADC
Sensor Voltage
Binary Value
Binary Value:
1001001100
Decimal Value:
588
Each bit can be 1 OR 0
Number of bits
VOLTAGE
TIME
BIT VALUE
0
1024
“Why 1024?”
Notes: What does an Analog pin do?
It translates continuous analog signals into discrete digital values that microcontrollers can understand and process.
Therefore, it will round down to the nearest bit value that corresponds to the continuous voltage input
These pins convert this by utilising an ADC (Analog to Digital Converter)
What are ADC characteristics?
ADC’s are bounded by two main things
  Their maximum voltage (normally bound to supply voltage) 5V in the case of the Arduino Nano
  Their resolution which means the number of bits they have.
    This number of bits is divided evenly through the maximum voltage

## Slide 5
WHAT DOES ADC [7] MEAN?
A0
A1
A2
A3
A4
A5
A6
A7
ADC
Multiplexer
B0
B1
B2
TO ARRAY
Notes: This is a more indepth look at the multiplexer where if the pins B0, B1 and B2 select which channel you want the ADC to convert.
The B pins are automatically assigned in the code when you try to read an analog pin.

## Slide 6
TWO COMMON COMMUNICATION TYPES
CLOCK
DATA
I2C
Controller
Peripheral (Sensor)
Peripheral (Sensor)
SCL
SDA
RECIEVE
TRANSMIT
UART
Controller
Peripheral (Sensor)
TX
RX
RX
TX
Secret Handshakes🤝
Notes: Here are 2 basic communication styles
I2C and UART.

## Slide 7
NOW TIE IT BACK TO STM32
Notes: Here are 2 basic communication styles
I2C and UART.

## Slide 8
NOW TIE IT BACK TO STM32
Notes: Here are 2 basic communication styles
I2C and UART.

## Slide 9
NEXT WEEK IN
Week 22 – Payload Preliminary Design Development (3 of 4)
Next week we will go over what you'll need to include in your Preliminary Design Review presentation at Curtin on Dec 2nd, 2024
Please send through your progress and questions to binarx@curtin.edu.au so we can support you